## Slide 1: Residential vCPE use case
Alla Goldner
Director, Technology, Strategy & Standardization
A business need behind the use case and use case implementation by ONAP Amsterdam release

## Slide 2: Introduction — Amsterdam Release 1 use cases
vVoLTE
Residential vCPE
vFW (For backward compatibility)

## Slide 3: What are we trying to achieve in R1 R-vCPE
Reduce residential gateway software management complexity
Cut time to market for introducing new features that have potential to impact residential gateway architecture
Facilitate troubleshooting of devices and connectivity within home network

## Slide 4: Introducing…
NERG
Network Enhanced Residential Gateway
Notes: Istock 670901202

## Slide 5: What’s different with NERG vs. traditional RG
TR-317 specifies NERG architecture
Functions provided traditionally by RG are distributed between
On-site device (Bridged Residential Gateway — BRG)
Cloud based component (virtual Gateway — vG)
BRG-LAN Interface
BRG-LSL Interface
Logical vG-LSL Interface
Logical vG-WAN Interface
Logical Subscriber Link (LSL)
BRG
vG

## Slide 6: NERG architecture benefits
Facilitates simplified operations, enhanced management, and troubleshooting
01
Provides security services as VAS — activate new functions in vG
02
Potential for incremental service offerings
Personalized services
Smart Home
Enhanced multimedia services
04
03
Enables automatic access to media content

## Slide 7: NERG use cases
Let’s look at them…
Device specific services
Automatic access to media
Security services
M2M
Enhanced management and troubleshooting
IPv6 migration

## Slide 8: NERG use cases
    Overview
vG has visibility into all devices on home LAN
Can categorize devices based on owner or device profile, applying specific policies
1. Device specific services
    Value added services
    Parental control — restricted access to content
    Enhanced home office — a work laptop is provided higher bandwidth and prioritization based on a specified QoS policy
    Assured multimedia — video devices receive the highest QoS priority
    Guest service restrictions — unknown devices can access the Internet, but no other services

## Slide 9: NERG use cases
    Overview
CSP can offer security services as a value added service (VAS)
Security services hosted on virtual gateways eliminate the need for a physical RG and the need for manual intervention
2. Security services
    Value added services
    Firewalling
    Intrusion detection
    Web filtering
    Anti-virus for remote workers
    Security conscious families and small businesses
Notes: The network service provider can offer security services as a value added service (VAS).
  Firewalling
  intrusion detection
  web filtering
  anti-virus for remote workers
  security conscious families and small businesses.
When a subscriber registers for a new security service, a new function is activated in the vG and traffic steering sends all, or a specified subset of, the traffic (e.g. for a given device type) to the service chain that has this security function
  As the security service is hosted in the vG and is activated on demand e.g. via a self-care portal, there is no dependency on changing out the physical RG, and no need for a manual intervention (such as a technician visit or software installation).

## Slide 10: NERG use cases
    Overview
NERG extends DLNA framework beyond home network to include resources that are hosted by the CSP
This service leverages NERG’s LAN extension and DLNA support in the vG. This can also be combined with improved QoS policies
3. Automatic access to media content
    Value added services
    Subscribers can access personal media content hosted in the NSP network and third party/service provider media content
    Virtualized DLNA storage provides a more flexible and scalable solution for storage capacity: the subscriber only pays for what he needs (pay as you grow)
Notes: DLNA is a framework for media interoperability between consumer devices within the home network. NERG provides the ability to extend this framework beyond the home network, to resources that are hosted by the network service provider.
The subscriber can access either his own media content hosted in the NSP network (e.g. vNAS), or other media content provided by the operator or some third-party.
Virtualized DLNA storage provides a more flexible and scalable solution for storage capacity: the subscriber only pays for what he needs (pay as you grow). In addition, backup and redundancy are now handled by the NSP.
This service leverages NERG’s LAN extension and DLNA support in the vG. This can also be combined with improved QoS policies.

## Slide 11: NERG use cases
    Overview
Increase in connected devices in the home results in increased complexity to the subscriber, and multiple M2M gateways
NERG architecture introduces new abstraction layer in CSP network to accommodate existing and future M2M technologies
4. M2M
    Value added services
    Accelerate M2M deployment by hiding network complexities
    Ease of upgrade and scalability
    Additional services on top of integrated M2M gateways
    Facilitate access for third party providers by managing remote access, security, privacy, and guaranteeing QoS
Notes: A rapidly growing number of smart connected objects have entered the home, in particular to support smart home applications. These devices are often based on multiple, non-interoperable standards.
  This creates complexity for the subscriber, who can end up with a plethora of M2M gateways.
The NERG architecture offers a unique opportunity to simplify M2M network design and deployment by introducing an abstraction layer in the operator network that can accommodate existing and future M2M technologies (i.e. different stacks).
  Being both highly scalable and easily upgradable, this model can accelerate M2M deployment since most the complexity is hidden from a non-technical end-user.
  The NSP can offer additional services on top of these integrated M2M gateways (e.g. one virtual button to switch off/on the lights in as many rooms as needed, across any M2M technology).
  The NSP can also facilitate access for third party providers (e.g. utility companies, health care providers) by managing remote access, security, privacy and guaranteeing QoS.

## Slide 12: NERG use cases
    Overview
NERG provides an alternative approach to RG replacement by adding IPv6 support in the vG
5. IPv6 migration
    Value added services
    Layer 3 support — existing RG can be changed to a bridge mode configuration (BRG)
    IPv6 support — without replacing RG
    Combine IPv6 NERG support with IPv4/IPv6 transition methods — easier to add new mechanisms on the vG rather compared to legacy physical RGs
Notes: If an RG does not support IPv6, NERG can provide an alternative approach to RG replacement by adding IPv6 support in the vG.
  The existing RG can be changed to a bridge mode configuration (BRG), so that Layer 3, including IPv6 forwarding and control (e.g. DHCPv6 PD, SLAAC), can be delivered by the vG.
  This may permit IPv6 support without requiring the replacement of the RG.
  The vG could also combine IPv6 NERG support with IPv4/IPv6 transition methods, as it is deemed to be easier to add these new mechanisms on the vG rather than on physical RGs.

## Slide 13: NERG use cases
    Overview
NERG allows for direct connectivity to network for all devices
Provides enhanced service management driven by the subscribers’ self-care portal as well as optimized troubleshooting by the operator’s support technicians
6. Enhanced management and troubleshooting
    Value added services
    Subscriber self configuration through portal — manage device parameters (IP addressing, filtering, QoS, remote access, etc.)
    Enhanced customer and call center support capabilities
    Reduced RG complexity — increased visibility and programmability lessens burden on support and call centers
Notes: Operators can take advantage of NERG by allowing all devices connected in the home network to be visible and reachable from the operator’s network side (in the traditional RG model, end devices are hidden behind NAT).
  This direct connectivity can be used to provide enhanced service management driven by the subscribers’ self-care portal as well as optimized troubleshooting by the operator’s support technicians.
  The subscriber can manage device parameters (IP addressing, filtering, QoS, remote access, etc.) from the portal, which can be accessed from anywhere.
  Based on the auto discovery of the LAN devices within the customer premises, the support call center is able to check the devices connected to the subscriber’s network and launch specific tests as if a support technician was directly connected to the customer network, by extending the customer LAN to the Service Provider’s management system for the period of time required.
  Reducing support complexity is one of the key benefits expected from NERG, based on the reduced Residential Gateway complexity and the increased visibility and programmability.

## Slide 14: vCPE use case — Amsterdam
Web Server
vDNS + vPDHCP
Infrastructure
Per Customer
Control
Data + Control
BRG
Emulator 2
(VPP)
SDNC
DMaaP
DCAE
(Collector)
ONAP OAM Neutron Network
Home Network 2
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
vG2
(VPP)
vG1
(VPP)
vBNG
(VPP)
Home Network 1
BRG
Emulator 1 (VPP)
vG MUX
(VPP)
CPE_Public Neutron Network

## Slide 15: vCPE use case VNFs
vDNS
Infrastructure
Per Customer
Control
Data + Control
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
ISC
https://www.isc.org/downloads/dhcp/
FreeRadius
https://freeradius.org/
BIND
https://www.isc.org/downloads/bind/
Web Server
vG1
(VPP)
vBNG
(VPP)
BRG
Emulator 1 (VPP)
vG MUX
(VPP)
Vector Packet Processing (VPP) + modifications
https://fd.io/technology/
Apache Web Server 2
All VNFs are open source, no physical components
HEAT templates produced for all VNFs

## Slide 16: Service Lifecycle Management
Real-time
Operation
Design—Onboarding
Continuous Real-time Fulfilment
Hybrid Cloud
Product Catalog
Offline
In Lab
Real-time
In Production
DESIGN
ORCHESTRATE
OPERATE
Notes: Amdocs approach to NFV/SDN is around service lifecycle management – we bring a complete holistic approach that starts with service design and onboarding through to instantiation and orchestration of virtual services, including continuous re-fulfilment based on policy-driven automation.
Finally the ability to perform real time operations including active inventory and assurance.

## Slide 17: Multiple ONAP services construct the use case
Infrastructure
Per Customer
Control
Data + Control
vG2
(VPP)
vG1
(VPP)
vBNG
(VPP)
vG MUX
(VPP)
BRG_BNG
Neutron Network
BNG_MUX
Neutron Network
MUX_GW
Neutron Network
BRG
Emulator 2
(VPP)
BRG
Emulator 1 (VPP)
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
CPE_SIGNAL
Neutron Network
Web Server
vDNS + vPDHCP
CPE_Public Neutron Network
GenInfra Service

## Slide 18: Multiple ONAP services construct the use case
Web Server
vDNS + vPDHCP
CPE_Public Neutron Network
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
CPE_SIGNAL
Neutron Network
Infrastructure
Per Customer
Control
Data + Control
vG2
(VPP)
vG1
(VPP)
vBNG
(VPP)
vG MUX
(VPP)
BRG_BNG
Neutron Network
MUX_GW
Neutron Network
BRG
Emulator 2
(VPP)
BRG
Emulator 1 (VPP)
BNG_MUX Service
BNG_MUX
Neutron Network

## Slide 19: Multiple ONAP services construct the use case
Web Server
vDNS + vPDHCP
CPE_Public Neutron Network
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
CPE_SIGNAL
Neutron Network
vG2
(VPP)
vG1
(VPP)
vBNG
(VPP)
BRG_BNG
Neutron Network
BRG
Emulator 2
(VPP)
BRG
Emulator 1 (VPP)
BNG_MUX
Neutron Network
Infrastructure
Per Customer
Control
Data + Control
vG_MUX Service
vG MUX
(VPP)
MUX_GW
Neutron Network

## Slide 20: Multiple ONAP services construct the use case
MUX_GW
Neutron Network
vG MUX
(VPP)
Web Server
vDNS + vPDHCP
CPE_Public Neutron Network
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
CPE_SIGNAL
Neutron Network
vG2
(VPP)
vG1
(VPP)
BRG
Emulator 2
(VPP)
BRG
Emulator 1 (VPP)
BNG_MUX
Neutron Network
Infrastructure
Per Customer
Control
Data + Control
BNG Service
vBNG
(VPP)
BRG_BNG
Neutron Network

## Slide 21: Multiple ONAP services construct the use case
BRG_BNG
Neutron Network
vBNG
(VPP)
MUX_GW
Neutron Network
vG MUX
(VPP)
Web Server
vDNS + vPDHCP
CPE_Public Neutron Network
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
CPE_SIGNAL
Neutron Network
vG2
(VPP)
vG1
(VPP)
BRG
Emulator 2
(VPP)
BNG_MUX
Neutron Network
Infrastructure
Per Customer
Control
Data + Control
BRG_EMU Service
BRG
Emulator 1 (VPP)

## Slide 22: Multiple ONAP services construct the use case
BRG
Emulator 1 (VPP)
BRG_BNG
Neutron Network
vBNG
(VPP)
MUX_GW
Neutron Network
vG MUX
(VPP)
Web Server
vDNS + vPDHCP
CPE_Public Neutron Network
vAAA
Authorization, Authentication, Accounting
vDHCP
Dynamic Host Config Protocol
CPE_SIGNAL
Neutron Network
vG2
(VPP)
BRG
Emulator 2
(VPP)
BNG_MUX
Neutron Network
Infrastructure
Per Customer
Control
Data + Control
vCPECust Service
TunnelXC
ONAP configures the Tunnel XC
PNF
ONAP configures the vG_MUX left IP Address and the VNI for the VxLAN tunneling
vG1
(VPP)
ONAP configures the vG_MUX right IP Address and the VNI for the VxLAN tunneling

## Slide 23: Development tasks
SDC
VNF
SO
A&AI
DCAE
CLAMP/ DCAE/ POLICY
SDNC
ROBOT
VNF onboarding and service design
Development
Generic workflows and custom workflows
Data schema
VES collector and analytics app
Closed loop control
Generic and custom APIs
Emulators and automated test suite

## Slide 24: Development tasks
Service Modeling and Call Flow Design

## Slide 25: Development tasks
Service Modeling and Call Flow Design
VPP-based VNF Development (vBRG, vBNG, vGMUX, vG)

## Slide 26: Development tasks
Service Modeling and Call Flow Design
VPP-based VNF Development (vBRG, vBNG, vGMUX, vG)
VNF Onboarding & Service Design in SDC
HEAT Templates

## Slide 27: Development tasks
Service Modeling and Call Flow Design
DCAE VES Collector
DCAE Analytics App
VPP-based VNF Development (vBRG, vBNG, vGMUX, vG)
VNF Onboarding & Service Design in SDC
HEAT Templates

## Slide 28: Development tasks
Closed Loop Design Using CLAMP
Output: Policy + DCAE Template
Service Modeling and Call Flow Design
DCAE VES Collector
DCAE Analytics App
VPP-based VNF Development (vBRG, vBNG, vGMUX, vG)
VNF Onboarding & Service Design in SDC
HEAT Templates

## Slide 29: Development tasks
Closed Loop Design Using CLAMP
Output: Policy + DCAE Template
Service Modeling and Call Flow Design
DCAE VES Collector
DCAE Analytics App
VPP-based VNF Development (vBRG, vBNG, vGMUX, vG)
VNF Onboarding & Service Design in SDC
HEAT Templates
BSS Emulator
Homing Emulator

## Slide 30: Development tasks
Closed Loop Design Using CLAMP
Output: Policy + DCAE Template
Generic & Custom Workflows for SO
Service Modeling and Call Flow Design
DCAE VES Collector
DCAE Analytics App
VPP-based VNF Development (vBRG, vBNG, vGMUX, vG)
Generic & Custom SDNC APIs (Yang & DGs)
VNF Onboarding & Service Design in SDC
HEAT Templates
Update of A&AI Data Schema
BSS Emulator
Homing Emulator

## Slide 31: Development tasks
Closed Loop Design Using CLAMP
Output: Policy + DCAE Template
Generic & Custom Workflows for SO
Service Modeling and Call Flow Design
DCAE VES Collector
DCAE Analytics App
VPP-based VNF Development (vBRG, vBNG, vGMUX, vG)
Generic & Custom SDNC APIs (Yang & DGs)
VNF Onboarding & Service Design in SDC
HEAT Templates
Update of A&AI Data Schema
BSS Emulator
Robot Test Suite
Homing Emulator

## Slide 32: Summary
NERG enables value added services leveraging the virtual gateway — minimize disruption to existing RG
Designed to facilitate improved security, trouble shooting and reduce burden on support/call centers
Leverages and extends ONAP functionalities in R1
R-vCPE a key use case in Amsterdam release
Notes: Istock 639721568

## Slide 33
Thank you
Join the conversation #NFVtalk
Amdocs NFV powered by ONAP The industry’s first packaged software and services solution for NFV service innovation

## Slide 34: Backup slides

## Slide 35: Introducing…
NERG:
Network Enhanced Residential Gateway
Option 1

## Slide 36: High level architecture
BRG-LAN Interface
BRG-LSL Interface
Logical vG-LSL Interface
Logical vG-WAN Interface
Logical Subscriber Link (LSL)
BRG
vG
Notes: BRG: Bridged Residential Gateway – this is the CPE still located at the residential customer premises, configured as a managed bridge connecting its LAN interfaces and the BRG-LSL interface.
vG: virtual Gateway – The set of networking and service related Network Functions that are hosted in the NSP network; the vG is the default IP gateway for the LAN devices. At a minimum, the vG provides Network Functions for:
  The termination of the LSL in the NSP’s network
  IP address management – DHCP service
  IP forwarding and IPv4 NAT capabilities
  the termination of the WAN interface
vG-WAN interface: Logical interface(s) on the vG to one or more IP networks.
LSL: Logical Subscriber Link – the subscriber specific logical point-to-point layer 2 connection between the BRG and the vG.
  This bridge conforms to IEEE 802.1D [3] and 802.1Q [4] and consequently supports MAC learning.
    Hence local traffic is switched locally, not hair-pinned to the vG.
  BRG-LAN interface: Interface(s) on the BRG for connecting LAN devices (i.e. in the home).
  BRG-LSL interface: Logical layer 2 interface on the BRG facing the vG.
  vG-LSL interface: Logical layer 2 interface on the vG facing the BRG.